## Slide 1
Coming from the encoder
(no elaborations, values from 0 to 359.9999999)
Cumulative (multi-turn) values after common zeroing (for reference)
Useful in post-processing to isolate the intervals where the reducer output side is between 0 and 360
(or opposite)
Data structure
See next slide

## Slide 2
Input side
Output side
BOSCH servomotor
(position-controlled)
BOSCH servomotor
(torque-controlled)
Renishaw
(absolute) Encoder
Manner Torquemeter
Manner Torquemeter
Renishaw
(absolute) Encoder
Fast shaft
Slow shaft
Fast shaft
Temperature sensor
Temperature sensor
1
2
3, 11
Tested Reducer (Red Ratio=81)
4
7
8
9
10
Legend
Secondary Reducer (Red Ratio=156)

## Slide 3
Test Procedure
It is programmed as a state machine within the TwinCAT PLC. The main steps are:
1) Warm-up: free run until the target oil temperature is reached in the tested reducer. 2) Homing: position the reducer at its absolute zero position (output-side Renishaw encoder). 3) Unloading: the input-side Bosch motor maintains the reached position, while the output-side Bosch motor (torque-controlled) is used to unload the low-speed shaft. 4) Zeroing: the Renishaw encoders are single-turn absolute encoders, but their zero positions do not correspond to each other (it is impossible to mount the transmissions with guaranteed angular alignment).
Therefore, a software offset (mask) in the PLC is used to set a common baseline, ensuring that from this point onward both encoders are set to 0. Since zeroing is performed after unloading (Step 3), the output (slow) shaft may have moved a bit from the homing (0 absolute value, reached during Step 2). As a result, the zeroed encoder position slightly different from the absolute 0 position (the raw value read by the encoder). This does not create issues for the subsequent analyses. See the values highlighted in red in the previous slide. From this point, cumulative positions are computed (i.e., multi-turn positions, adding 360° each time a full revolution is completed).
Renishaw
(input side)
Renishaw
(input side)
Zero absolute value
Zero absolute value
The zeroing mask provides a position for which both encoders are initiated (though their own absolute values differ)

## Slide 4
Test Procedure (continue)
5) Run at target speed the input side motor
6) Ramp the torque on the slow shaft untill the target value is reached. The PLC modulates the output side BOSH servomotor torque setpoint through a PID utilizing the Manner torquemeter (installed on the slow shaft) as a feedback.
7) Once all test conditions are enforced, the data recording starts
8) Data valid set to 1 to indicate the interval between 0 and 360 of the absolute value of the Renishaw load-side encoder (LAST COLUMN OF EXCEL DATA) for TE computation. Once the complete revolution is performed, data valid is set back to 0.
Note: the same procedure (steps 5 to 8) is repeated for the backward motion.